## Slide 1: EDES 301 DDR Handheld Proposal
10/5
Boyuan Zhang

## Slide 2: Background Information
What is being proposed?
  A mini handheld game like Dance Dance Revolution
    LEDs indicate the upcoming direction for the joystick to move
    A screen as a score indicator and another as a time countdown
    A buzzer for incorrect input and a buzzer as a metronome
  Links to existing projects / libraries
    Similar to this project, with slightly different LED operations.
      The 4-button setup is essentially the same as the joystick input
      Want to keep the 7-segment display “play” and “lost” function but also add score tracking.
    In terms of joystick input and buzzer, this project contains usable codes
Overall, the hardware design is not difficult, with only 4 main components.
  However, the nature of the game is dependent on timing, and actually building out a “song” to play

## Slide 3: System Block Diagram
Pocket beagle
GPIO headers
I2C
16 LEDs
GPIO headers (P1_2,4,6,8,29,31,33,35; P2_2,4,6,8,28,30,32,34)
Buzzers
GPIO P1_10, 12
Joystick (4 directions and press)
GPIO P2_1,3,5,7,9
Displays
I2C2_SDA (P1_28)
I2C2_SCL (P1_26)

## Slide 4: Power Block Diagram
Pocket beagle
GPIO headers
I2C
16 LEDs
3.3v, 2-5mA per
2 Buzzer
3.3v, 15mA per
Joystick
3.3v, <1mA
2 Display
3.3v, 100mA per

## Slide 5: Components / Budget
Component | EDES301 to Buy? | Cost
Joystick | Yes | $14 for 10 Pcs
16 LEDs | No | ~$3
Buzzer | No | $0.95
Display | No | $10.95
See Next Slide for Instructions